## Slide 1: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 2: Welcome to Assembly Language
Some Good Questions to Ask
Assembly Language Applications

## Slide 3: Questions to Ask
Why am I learning Assembly Language?
What background should I have?
What is an assembler?
What hardware/software do I need?
What types of programs will I create?
What do I get with this book?
What will I learn?

## Slide 4: Welcome to Assembly Language (cont)
How does assembly language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?
Why learn AL?

## Slide 5: Assembly Language Applications
Some representative types of applications:
  Business application for single platform
  Hardware device driver
  Business application for multiple platforms
  Embedded systems & computer games
(see next panel)

## Slide 6: Comparing ASM to High-Level Languages

## Slide 7: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 8: Virtual Machine Concept
Virtual Machines
Specific Machine Levels

## Slide 9: Virtual Machines
Tanenbaum: Virtual machine concept
Programming Language analogy:
  Each computer has a native machine language (language L0) that runs directly on its hardware
  A more human-friendly language is usually constructed above machine language, called Language L1
Programs written in L1 can run two different ways:
  Interpretation – L0 program interprets and executes L1 instructions one by one
  Translation – L1 program is completely translated into an L0 program, which then runs on the computer hardware

## Slide 10: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
mov eax,A
mul B
add eax,C
call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 11: Specific Machine Levels
(descriptions of individual levels follow . . . )

## Slide 12: High-Level Language
Level 4
Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
Programs compile into assembly language (Level 4)

## Slide 13: Assembly Language
Level 3
Instruction mnemonics that have a one-to-one correspondence to machine language
Programs are translated into Instruction Set Architecture Level - machine language (Level 2)

## Slide 14: Instruction Set Architecture (ISA)
Level 2
Also known as conventional machine language
Executed by Level 1 (Digital Logic)

## Slide 15: Digital Logic
Level 1
CPU, constructed from digital logic gates
System bus
Memory
Implemented using bipolar transistors
next: Data Representation

## Slide 16: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 17: Data Representation
Binary Numbers
  Translating between binary and decimal
Binary Addition
Integer Storage Sizes
Hexadecimal Integers
  Translating between decimal and hexadecimal
  Hexadecimal subtraction
Signed Integers
  Binary subtraction
Character Storage

## Slide 18: Binary Numbers
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 19: Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 20: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 21: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 22: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 23: Signed Integers
The highest bit indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D

## Slide 24: Forming the Two's Complement
Negative numbers are stored in two's complement notation
Represents the additive Inverse
Note that 00000001 + 11111111 = 00000000

## Slide 25: Binary Subtraction
When subtracting A – B, convert B to its two's complement
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1
Practice: Subtract 0101 from 1001.

## Slide 26: Ranges of Signed Integers
The highest bit is reserved for the sign. This limits the range:
Practice: What is the largest positive value that may be stored in 20 bits?

## Slide 27: Character Storage
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode (0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 28: Numeric Data Representation
pure binary
  can be calculated directly
ASCII binary
  string of digits: "01010101"
ASCII decimal
  string of digits: "65"
ASCII hexadecimal
  string of digits: "9C"

## Slide 29: Summary
Assembly language helps you learn how software is constructed at the lowest levels
Assembly language has a one-to-one relationship with machine language
Each layer in a computer's architecture is an abstraction of a machine
  layers can be hardware or software
Boolean expressions are essential to the design of computer hardware and software

## Slide 30: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 31: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 32: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 33: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 34: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output
Instruction Execution Cycle

## Slide 35: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  Place the address of the value you want to read on the address bus.
  Assert (changing the value of) the processor’s RD (read) pin.
  Wait one clock cycle for the memory chips to respond.
  Copy the data from the data bus into the destination operand

## Slide 36: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 37: How a Program Runs

## Slide 38: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 39: Modes of Operation
Protected mode
  native mode (Windows, Linux)
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 40: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 41: General-Purpose Registers
Named storage locations inside the CPU, optimized for speed.

## Slide 42: Accessing Parts of Registers
Use 8-bit name, 16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX

## Slide 43: Index and Base Registers
Some registers have only a 16-bit name for their lower half:

## Slide 44: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 45: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit

## Slide 46: Status Flags
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Auxiliary Carry
  carry from bit 3 to bit 4
Parity
  sum of 1 bits is an even number

## Slide 47: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 48: IA-32 Memory Management
Real-address mode
Calculating linear addresses
Protected mode
Multi-segment model
Paging

## Slide 49: Protected Mode (1 of 2)
4 GB addressable RAM
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows

## Slide 50: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 51: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 52: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 53: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 54: Intel 965 Express Chipset

## Slide 55: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 56: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 57: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 58: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 59: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 60: Summary
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Instruction execution cycle
Multitasking
Floating Point Unit (FPU)
Complex Instruction Set
Real mode and Protected mode
Motherboard components
Memory types
Input/Output and access levels

## Slide 61: Basic Elements of Assembly Language
Integer constants
Integer expressions
Character and string constants
Reserved words and identifiers
Directives and instructions
Labels
Mnemonics and Operands
Comments
Examples

## Slide 62: Integer Constants
Optional leading + or – sign
binary, decimal, hexadecimal, or octal digits
Common radix characters:
  h – hexadecimal
  d – decimal
  b – binary
  r – encoded real
Examples: 30d, 6Ah, 42, 1101b
Hexadecimal beginning with letter: 0A5h

## Slide 63: Integer Expressions
Operators and precedence levels:
Examples:

## Slide 64: Character and String Constants
Enclose character in single or double quotes
  'A', "x"
  ASCII character = 1 byte
Enclose strings in single or double quotes
  "ABC"
  'xyz'
  Each character occupies a single byte
Embedded quotes:
  'Say "Goodnight," Gracie'

## Slide 65: Reserved Words and Identifiers
Reserved words cannot be used as identifiers
  Instruction mnemonics, directives, type attributes, operators, predefined symbols
  See MASM reference in Appendix A
Identifiers
  1-247 characters, including digits
  not case sensitive
  first character must be a letter, _, @, ?, or $

## Slide 66: Directives
Commands that are recognized and acted upon by the assembler
  Not part of the Intel instruction set
  Used to declare code, data areas, select memory model, declare procedures, etc.
  not case sensitive
Different assemblers have different directives
  NASM not the same as MASM, for example

## Slide 67: Instructions
Assembled into machine code by assembler
Executed at runtime by the CPU
We use the Intel IA-32 instruction set
An instruction contains:
  Label (optional)
  Mnemonic (required)
  Operand (depends on the instruction)
  Comment (optional)

## Slide 68: Labels
Act as place markers
  marks the address (offset) of code and data
Follow identifer rules
Data label
  must be unique
  example: myArray (not followed by colon)
Code label
  target of jump and loop instructions
  example: L1: (followed by colon)

## Slide 69: Mnemonics and Operands
Instruction Mnemonics
  memory aid
  examples: MOV, ADD, SUB, MUL, INC, DEC
Operands
  constant
  constant expression
  register
  memory (data label)
Constants and constant expressions are often called immediate values

## Slide 70: Comments
Comments are good!
  explain the program's purpose
  when it was written, and by whom
  revision information
  tricky coding techniques
  application-specific explanations
Single-line comments
  begin with semicolon (;)
Multi-line comments
  begin with COMMENT directive and a programmer-chosen character
  end with the same programmer-chosen character

## Slide 71: Instruction Format Examples
No operands
  stc ; set Carry flag
One operand
  inc eax ; register
  inc myByte ; memory
Two operands
  add ebx,ecx ; register, register
  sub myByte,25 ; memory, constant
  add eax,36 * 25 ; register, constant-expression

## Slide 72: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants

## Slide 73: Example: Adding and Subtracting Integers
; AddTwo.asm – adds two 32-bit integers
.386
.model flat,stdcall
.stack 4096
ExitProcess PROTO, dwExitCode:DWORD
.code
main PROC
mov eax,5 ; move 5 to the EAX register
add eax,6 ; add 6 to the EAX register
INVOKE ExitProcess,0
main ENDP
END main

## Slide 74: Example Output
Showing registers and flags in the debugger:
EAX=00030000 EBX=7FFDF000 ECX=00000101 EDX=FFFFFFFF
ESI=00000000 EDI=00000000 EBP=0012FFF0 ESP=0012FFC4
EIP=00401024 EFL=00000206 CF=0 SF=0 ZF=0 OF=0

## Slide 75: Suggested Coding Standards (2 of 2)
Indentation and spacing
  code and data labels – no indentation
  executable instructions – indent 4-5 spaces
  comments: right side of page, aligned vertically
  1-3 spaces between instruction and its operands
    ex: mov ax,bx
  1-2 blank lines between procedures

## Slide 76: Program Template
; Program Template (Template.asm)
; Program Description:
; Author:
; Creation Date:
; Revisions:
; Date: Modified by:
.386
.model flat,stdcall
.stack 4096
ExitProcess PROTO, dwExitCode:DWORD
.data
; declare variables here
.code
main PROC
; write your code here
INVOKE ExitProcess,0
main ENDP
; (insert additional procedures here)
END main

## Slide 77: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants

## Slide 78: Assembling, Linking, and Running Programs
Assemble-Link-Execute Cycle
Listing File
Map File

## Slide 79: Assemble-Link Execute Cycle
The following diagram describes the steps from creating a source program through executing the compiled program.
If the source code is modified, Steps 2 through 4 must be repeated.

## Slide 80: Listing File
Use it to see how your program is compiled
Contains
  source code
  addresses
  object code (machine language)
  segment names
  symbols (variables, procedures, and constants)

## Slide 81: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants

## Slide 82: Defining Data
Intrinsic Data Types
Data Definition Statement
Defining BYTE and SBYTE Data
Defining WORD and SWORD Data
Defining DWORD and SDWORD Data
Defining QWORD Data
Defining TBYTE Data
Defining Real Number Data
Little Endian Order
Adding Variables to the AddSub Program
Declaring Uninitialized Data

## Slide 83: Intrinsic Data Types (1 of 2)
BYTE, SBYTE
  8-bit unsigned integer; 8-bit signed integer
WORD, SWORD
  16-bit unsigned & signed integer
DWORD, SDWORD
  32-bit unsigned & signed integer
QWORD
  64-bit integer
TBYTE
  80-bit integer

## Slide 84: Intrinsic Data Types (2 of 2)
REAL4
  4-byte IEEE short real
REAL8
  8-byte IEEE long real
REAL10
  10-byte IEEE extended real

## Slide 85: Data Definition Statement
A data definition statement sets aside storage in memory for a variable.
May optionally assign a name (label) to the data
Syntax:
  [name] directive initializer [,initializer] . . .
  value1 BYTE 10
All initializers become binary data in memory

## Slide 86: Defining BYTE and SBYTE Data
value1 BYTE 'A' ; character constant
value2 BYTE 0 ; smallest unsigned byte
value3 BYTE 255 ; largest unsigned byte
value4 SBYTE -128 ; smallest signed byte
value5 SBYTE +127 ; largest signed byte
value6 BYTE ? ; uninitialized byte
Each of the following defines a single byte of storage:
MASM does not prevent you from initializing a BYTE with a negative value, but it's considered poor style.
If you declare a SBYTE variable, the Microsoft debugger will automatically display its value in decimal with a leading sign.

## Slide 87: Defining Byte Arrays
list1 BYTE 10,20,30,40
list2 BYTE 10,20,30,40
BYTE 50,60,70,80
BYTE 81,82,83,84
list3 BYTE ?,32,41h,00100010b
list4 BYTE 0Ah,20h,‘A’,22h
Examples that use multiple initializers:

## Slide 88: Defining Strings (1 of 3)
A string is implemented as an array of characters
  For convenience, it is usually enclosed in quotation marks
  It often will be null-terminated
Examples:
str1 BYTE "Enter your name",0
str2 BYTE 'Error: halting program',0
str3 BYTE 'A','E','I','O','U'
greeting BYTE "Welcome to the Encryption Demo program "
BYTE "created by Kip Irvine.",0

## Slide 89: Defining Strings (2 of 3)
To continue a single string across multiple lines, end each line with a comma:
menu BYTE "Checking Account",0dh,0ah,0dh,0ah,
"1. Create a new account",0dh,0ah,
"2. Open an existing account",0dh,0ah,
"3. Credit the account",0dh,0ah,
"4. Debit the account",0dh,0ah,
"5. Exit",0ah,0ah,
"Choice> ",0

## Slide 90: Defining Strings (3 of 3)
End-of-line character sequence:
  0Dh = carriage return
  0Ah = line feed
str1 BYTE "Enter your name: ",0Dh,0Ah
BYTE "Enter your address: ",0
newLine BYTE 0Dh,0Ah,0
Idea: Define all strings used by your program in the same area of the data segment.

## Slide 91: Using the DUP Operator
Use DUP to allocate (create space for) an array or string. Syntax: counter DUP ( argument )
Counter and argument must be constants or constant expressions
var1 BYTE 20 DUP(0) ; 20 bytes, all equal to zero
var2 BYTE 20 DUP(?) ; 20 bytes, uninitialized
var3 BYTE 4 DUP("STACK") ; 20 bytes: "STACKSTACKSTACKSTACK"
var4 BYTE 10,3 DUP(0),20 ; 5 bytes

## Slide 92: Defining WORD and SWORD Data
Define storage for 16-bit integers
  or double characters
  single value or multiple values
word1 WORD 65535 ; largest unsigned value
word2 SWORD –32768 ; smallest signed value
word3 WORD ? ; uninitialized, unsigned
word4 WORD "AB" ; double characters
myList WORD 1,2,3,4,5 ; array of words
array WORD 5 DUP(?) ; uninitialized array

## Slide 93: Defining DWORD and SDWORD Data
val1 DWORD 12345678h ; unsigned
val2 SDWORD –2147483648 ; signed
val3 DWORD 20 DUP(?) ; unsigned array
val4 SDWORD –3,–2,–1,0,1 ; signed array
Storage definitions for signed and unsigned 32-bit integers:

## Slide 94: Little Endian Order
All data types larger than a byte store their individual bytes in reverse order. The least significant byte occurs at the first (lowest) memory address.
Example:
val1 DWORD 12345678h

## Slide 95: Adding Variables to AddSub
; This program adds and subtracts 32-bit unsigned
; integers and stores the sum in a variable.
.data
val1 DWORD 10000h
val2 DWORD 40000h
val3 DWORD 20000h
finalVal DWORD ?
.code
main PROC
mov eax,val1 ; start with 10000h
  add eax,val2 ; add 40000h
  sub eax,val3 ; subtract 20000h
  mov finalVal,eax ; store the result (30000h)
  invoke ExitProcess, 0
main ENDP
END main

## Slide 96: Declaring Unitialized Data
Use the .data? directive to declare an unintialized data segment:
  .data?
Within the segment, declare variables with "?" initializers:
  smallArray DWORD 10 DUP(?)
Advantage: the program's EXE file size is reduced.

## Slide 97: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants

## Slide 98: Symbolic Constants
EQU Directive

## Slide 99: EQU Directive
Define a symbol as either an integer or text expression.
Cannot be redefined
PI EQU <3.1416>
pressKey EQU <"Press any key to continue...",0>
.data
prompt BYTE pressKey

## Slide 100: Summary
Integer expression, character constant
directive – interpreted by the assembler
instruction – executes at runtime
code, data, and stack segments
source, listing, object, map, executable files
Data definition directives:
  BYTE, SBYTE, WORD, SWORD, DWORD, SDWORD
  DUP operator
Symbolic constant
  EQU

## Slide 101: Chapter Overview
Data Transfer Instructions
Addition and Subtraction

## Slide 102: Data Transfer Instructions
Operand Types
Instruction Operand Notation
Direct Memory Operands
MOV Instruction
Zero & Sign Extension
XCHG Instruction
Direct-Offset Instructions

## Slide 103: Operand Types
Immediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
Register – the name of a register
  register name is converted to a number and encoded within the instruction
Memory – reference to a location in memory
  memory address is encoded within the instruction, or a register holds the address of a memory location

## Slide 104: Instruction Operand Notation

## Slide 105: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
The named reference (label) is automatically dereferenced by the assembler
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format

## Slide 106: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Move from source to destination. Syntax:
    MOV destination,source
No more than one memory operand permitted
CS, EIP, and IP cannot be the destination
No immediate to segment moves

## Slide 107: Zero Extension
mov bl,10001111b
movzx ax,bl ; zero-extension
When you copy a smaller value into a larger destination, the MOVZX instruction fills (extends) the upper half of the destination with zeros.
The destination must be a register.

## Slide 108: Sign Extension
mov bl,10001111b
movsx ax,bl ; sign extension
The MOVSX instruction fills the upper half of the destination with a copy of the source operand's sign bit.
The destination must be a register.

## Slide 109: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
xchg ax,bx ; exchange 16-bit regs
xchg ah,al ; exchange 8-bit regs
xchg var1,bx ; exchange mem, reg
xchg eax,ebx ; exchange 32-bit regs
xchg var1,var2 ; error: two memory operands
XCHG exchanges the values of two operands. At least one operand must be a register. No immediate operands are permitted.

## Slide 110: Direct-Offset Operands
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB+1 ; AL = 20h
mov al,[arrayB+1] ; alternative notation
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
Q: Why doesn't arrayB+1 produce 11h?

## Slide 111: Direct-Offset Operands (cont)
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax,[arrayW+2] ; AX = 2000h
mov ax,[arrayW+4] ; AX = 3000h
mov eax,[arrayD+4] ; EAX = 00000002h
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
; Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??
What will happen when they run?

## Slide 112: Evaluate this . . .
We want to write a program that adds the following three bytes:
.data
myBytes BYTE 80h,66h,0A5h
What is your evaluation of the following code?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
mov ax,myBytes
add ax,[myBytes+1]
add ax,[myBytes+2]
Any other possibilities?

## Slide 113: Evaluate this . . . (cont)
.data
myBytes BYTE 80h,66h,0A5h
How about the following code. Is anything missing?
movzx ax,myBytes
mov bl,[myBytes+1]
add ax,bx
mov bl,[myBytes+2]
add ax,bx ; AX = sum
Yes: Move zero to BX before the MOVZX instruction.

## Slide 114: What's Next
Data Transfer Instructions
Addition and Subtraction

## Slide 115: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 116: INC and DEC Instructions
Add 1, subtract 1 from destination operand
  operand may be register or memory
INC destination
    Logic: destination  destination + 1
DEC destination
    Logic: destination  destination – 1

## Slide 117: INC and DEC Examples
.data
myWord WORD 1000h
myDword DWORD 10000000h
.code
inc myWord ; 1001h
dec myWord ; 1000h
inc myDword ; 10000001h
mov ax,00FFh
inc ax ; AX = 0100h
mov ax,00FFh
inc al ; AX = 0000h

## Slide 118: ADD and SUB Instructions
ADD destination, source
  Logic: destination  destination + source
SUB destination, source
  Logic: destination  destination – source
Same operand rules as for the MOV instruction

## Slide 119: ADD and SUB Examples
.data
var1 DWORD 10000h
var2 DWORD 20000h
.code ; ---EAX---
mov eax,var1 ; 00010000h
add eax,var2 ; 00030000h
add ax,0FFFFh ; 0003FFFFh
add eax,1 ; 00040000h
sub ax,1 ; 0004FFFFh

## Slide 120: NEG (negate) Instruction
.data
valB BYTE -1
valW WORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767
Reverses the sign of an operand. Operand can be a register or memory operand.
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?

## Slide 121: NEG Instruction and the Flags
.data
valB BYTE 1,0
valC SBYTE -128
.code
neg valB ; CF = 1, OF = 0
neg [valB + 1] ; CF = 0, OF = 0
neg valC ; CF = 1, OF = 1
The processor implements NEG using the following internal operation:
SUB 0,operand
Any nonzero operand causes the Carry flag to be set.

## Slide 122: Implementing Arithmetic Expressions
.data
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; -36
HLL compilers translate mathematical expressions into assembly language. You can do it also. For example:
Rval = -Xval + (Yval – Zval)